## Slide 1: Internet of Things and home automation
Martin Harizanov

## Slide 2: Agenda
Introduce myself
What is IoT
Why IoT?
My home automation system architecture
Q/A

## Slide 3: About
IT Project Manager/Business Analyst/Business Intelligence/Data warehousing
Hobbies include IoT/home automation
I am active in the IoT Open Source/Hardware community
Blogger
My education background combines software and hardware

## Slide 4: What is IoT?
Internet of Things
  Internet connected objects (things) working together to solve a business problem
  Has been around for quite a while, but only recently has become affordable for personal use
Notes: It isn’t coming soon .. it is already here and has been so for quite a while
Connects billions of sensors and devices from every day consumer objects to industrial equipment

## Slide 5: What are the “Things” in the IoT?
Could be anything
  Physical
  Virtual
Notes:   Physical
    Objects such as
      Climate control
      Security/Disaster alarm system
      Energy/Resource metering (Electricity, Gas, Water)
      Water boiler, Solar boiler
      Car (OBDII, vehiclepi)
      The Sun (sunrise/set times, azimuth)
    Living things
      People (self quantification)
        Presence
        Location
        Health metrics
          Weight
          Activity tracking
          Temperature
          Blood Glycose monitors
          Fitbit
      Pets
  Virtual
    Personal schedule/calendar
    Social
      Email
      Twitter/FB
      Online notification platforms
    WWW resources
      Weather forecasting
      Stocks
      Traffic
      DB Storage
      Visualization dashboards
    Presence

## Slide 6: Why IoT?
Generate, collect, process and use acquired information to make better decisions
Smart objects: Make things that weren’t meant to talk to each other interact smartly
Gartner says the Internet of Things installed base will grow to 26 Billion units by 2020; I want to be well aligned and prepared for that
Notes: Provide intelligence
Improve efficiency

## Slide 7: Generate, collect, process and use acquired information to make decisions
    DIKW model
      Information is inferred from data, in the process of answering interrogative questions (e.g., "who", "what", "where", "how many", "when"), thereby making the data useful for "decisions and/or action".
      Knowledge as "synthesis of multiple sources of information over time"
Notes: There is more to data that meets the eye
  E.g. Momentary power of solar boiler based on the rate of temperature increase of fixed volume of water
  Shape of power waveform reveals the appliance
  Dew point from temperature and humidity
  Presence from ping times
If you can’t measure it, you can’t improve it
  Example (home scale, imagine on industrial scale)
    Power usage
      AC compressor heater element consumes ~140W, even when AC is off
      TV using 120W in standby mode
      Circulation pump UPS consuming 100W in standby mode
      Laser printer occasionally using 400W in standby mode to warm up toner
      Dishwasher in delayed start mode consumes 150W till program starts
      ..and many more

## Slide 8: Smart objects: Make things that weren’t meant to talk to each other interact smartly
  Phone  Location detection, presence detection  Thermostat
  Doorbell activation  CCTV takes picture Email + SMS + Tweet
  Fire Alarm  Email + SMS
  Security System CCTV  Email + SMS
  Climate control  presence @ home & weather forecast
  Hot water tank 1   Hot water tank 2   our presence, weather forecast
  Dog CCTV + Email
  Weather notifications  email

## Slide 9: Influence others to reduce their carbon footprint by sharing socially your metrics
Alex Laskey: How behavioral science can lower your energy bill
https://www.youtube.com/watch?v=4cJ08wOqloc
My @iot_house tweets power consumption statistics

## Slide 10: Challenges
Global cooperation
  Proprietary and incompatible protocols
  Lack of APIs
  Example: Common external power supply
Technological challenges
  Power usage
  Scalability
  Security
  Communication mechanisms
Ethics, control society, surveillance, consent and data driven life
Notes:   Proprietary and incompatible protocols even from same manufacturer as part of their business model

## Slide 11: Overall Architecture
Business logic
Thing
Interface
M2M
Protocol
Interface
Visualization, BI
Control UI
Protocol
Read properties
Set Property
Protocol
Protocol
Raw
Processed
Logic
Storage
Notes: Data produced by the connected things is acquired, processed and logged; DQ, what data to collect (collecting nothing with great accuracy)
Run on a R/O fs raspberry pi; considering moving to the cloud
As “Things” become increasingly smarter, they can talk directly to M2M layer
It is possible to have multiple interfaces on the same “Thing”, specializing on interfacing with certain its property (AC power, temperature, control)
It is possible that multiple interfaced “Things” have one and the same interface on the M2M end, as long as they use same protocol
Storage: Abstract and treat a “thing” with “interface”. EmonCMS, ThingSpeak, NoSQL; Retrieval of data API;
Visualization: in-built EmonCMS, Thingspeak; collect an relate data for better insight. Actionable analytics.

## Slide 12: The hardware interface to “things”
The ‘Funky’ project
It is an Arduino-compatible multi purpose micro that is:
  Very small: 20×21.2mm (0.78″x0.83″)
  Very light: 3 grams
  Low power (up to 1 year on coin cell battery)
  Wireless capable (RFM12B transceiver)
Notes: I’ve created a miniature Arduino compatible clone with wireless connectivity to use as interface to physical objects. The project is open hardware/source.
YAPM,

## Slide 13: YAPM (Yet Another Power Monitor)
Wireless Power Monitor project

## Slide 14: Receiver module
The ‘RFM2Pi’ project
  It is an Arduino-compatible board that acts as a wireless bridge between wireless remote nodes and the M2M layer

## Slide 15: ESP8266 WiFi relay/thermostat project

## Slide 16: Software Interface example
NodeRED weather forecast/current conditions

## Slide 17: Machine to Machine
Using mosquitto MQTT broker, extremely lightweight publish/subscribe messaging transport protocol
My MQTT topic tree structure:

## Slide 18: Business logic layer
Using Node-RED
  Very visual, drag-and-connect
  Encapsulates all logic in single JSON file
  Examples
    Remote sensor data processing
    Speech recognition/generation
    Control UI
    Dynamic DNS updater
Notes: Speech NR demo

## Slide 19: Control UI
Notes: Need to work on consolidating these
OpenHab?

## Slide 20: Storage

## Slide 21: Visualization

## Slide 22: End
Thanks!

## Slide 23: Questions?